1970 Mustang

Production Figures

63A 2dr Fastback            39,470

65A 2dr Hardtop             77,161

76A Convertible              6,199

63B 2dr Fastback             6,464

65B 2dr Hardtop              5,408

76B Convertible              1,474

63C Fastback Mach 1         40,970

65E 2dr Hardtop Grande      13,581

Total                      190,727

Specials

Boss 302      7,013

Boss 429        499

Serial Numbers

0F04F100001

0-Last digit of model year

F-Assembly plant code(F-Dearborn, R-San Jose, M-Metuchen)

04-Plate code for Mustang(01 Hardtop, 02 Fastback, 03 Convertible, 04 Grande, 05 Mach 1)

F-Engine code

100001-Assembly plant consecutive unit number

Location

Stamped on plate riveted to instrument panel on driver's side, visible through the windshield. A Vehicle Certification Label replaced the previous Warranty Plate. It was mounted on the rear face of the driver's door.

Engine Codes

T- 200 ci 1V six cyl 120hp

L- 250 ci 1V six cyl 155hp

F- 302 ci 2V V-8 220hp

G- 302 ci 4V V-8 290hp (Boss)

H- 351 ci 2V V-8 250hp(351W & 351C)

M- 351 ci 4V V-8 300hp

Q- 428 ci 4V V-8 335hp(Cobra Jet)

R- 428 ci 4V V-8 335hp(Cobra Jet Ram Air)

Z- 429 ci 4V V-8 375hp(Boss)

V-8 Distributors

302 ci 220hp - D0AF-12127-T

302 ci 290hp - C9ZF-12127-70F71

351 ci 250hp - D0AF-12127-H/manual, D0AF-12127-AO/automatic

351 ci 300hp - D0OF-12127-V/manual, D0OF-12127-Z/automatic

428 ci 335hp - D0ZF-12127-C/manual. D0ZF-12127-G/automatic

429 ci 375hp - C9ZF-12127-D

V-8 Carburetors

302 ci 220hp - D0AE-9510-C/manual,D0AE-9510-D or V/automatic

302 ci 290hp - C9ZF-9510-J (Holley R-4511)

351 ci 250hp - D0OF-9510-F/manual, D0OF-9510-L/automatic

351 ci 300hp - D0OF-9510-AB/manual,D0OF-9510-AC/automatic

428 ci 335hp - D0ZF-9510-AA or AD/manual(Holley R-4513,R-4515(with

A/C), D0ZF-9510-AB or AC automatic(Holley R-4514,R-

4516(with A/C)

429 ci 375hp - D0OF-9510-S (Holley R-4647)

Steering Gear Ratios

SMB-D – 19.9:1

SMB-F – 16.1:1

SMB-K – 16.1:1

1970 Mustang Prices                                     Retail

Hardtop    65A                                         $2,721.00

SportsRoof 63A                                          2,771.00

Convertible 76A                                         3,025.00

Grande     65E                                          2,926.00

Mach 1     63C                                          3,271.00

Boss 302                                                3,720.00

250 CID 155 hp Six. Extra charge over 200 CID Six          39.00

302 CID 220 hp V8. Extra charge over 200 CID Six          101.00

351 CID 250 hp V-8. Extra charge over 302 CID V-8          45.00

351 CID 300 hp V-8. Extra charge over 302 CID V-8          93.00

Mach 1 over 351 CID 250 hp             48.00

428 CID 335 hp Cobra V8. Extra charge over 302 CID V8     356.00

Mach 1 over 351 CID 250 hp            311.00

428 CID 335 hp Cobra Jet Ram-Air(except Mach 1)           421.00

Mach 1, over 351 CID 250 hp           376.00

Boss 429 CID 4V V8                                      1,208.00

SelectShift Cruise-O-Matic(except 428)                    201.00

with 428 V-8s                   222.00

Four-speed manual transmission, w/302,351,428 V-8s        205.00

Power front disc brakes(NA 200 CID six)                    65.00

Power steering                                             95.00

Air conditioner, SelectAire(NA w/200 CID,Boss 302 428 CID

w/4-speed manual)              380.00

Clock, electric-rectangular(NA Grande, Mach 1 or Decor Group)16.00

Clock, electric-round(std Grande, Mach 1)w/Decor Group only 16.00

Console                                                    54.00

Convenience Group w/Grande, Mach 1,Boss 302,& Decor Group  32.00

All others                               45.00

Defogger, rear window(2dr Hardtops)                        26.00

Mirrors, color-keyed dual racing                           26.00

Belts, Deluxe with reminder light                          15.00

Seat, rear Sport Deck(SportsRoof)                          97.00

Steering wheel, Rim Blow Deluxe                            39.00

Steering wheel, tilt                                       45.00

Windshield wipers, intermittent                            26.00

Space Saver spare(std Boss 302, NA 200 CID Six)

w/E70 or F70x14 WSW or RWL tires          7.00

w/E78x14 WSW tires                       13.00

w/E78x14 BSW tires                       20.00

Radio, AM                                                  61.00

Radio, AM/FM                                              214.00

Stereo-Sonic Tape(AM Radio required)                      134.00

Bumper Guards, front                                       13.00

Decor Group, Boss 302 and other models                     78.00

Convertibles                                  97.00

Molding, Rocker Panel(std with Decor Group, NA Grande, Mach 1

or Boss 302)                         16.00

Paint stripes, dual accent, Mach 1                         13.00

Roof, vinyl(hardtop & Grande)                              26.00

Sport Slats(requires dual racing mirrors)                  65.00

Trim rings/hub caps(std Boss 302)                          26.00

Wheel covers,(std Grande)                                  26.00

Wheel covers, Sports, Grande, Boss 302                     32.00

All others                            58.00

Wheel covers, wire, Grande                                 53.00

All others                                                 79.00

Wheels, Magnum 500 chrome Boss 302 only                   129.00

Wheels, Argent style steel(NC Mach 1) Grande               32.00

All others           58.00

Axle, Drag Pack, w/428 CID w/3.91:1 & 4.30:1 ratios       155.00

Axle, optional ratio                                       13.00

Axle, Traction-Lok differential                            43.00

Battery, heavy duty 55 amp                                 13.00

Battery, heavy duty 70 amp                                 13.00

Extra cooling package                                      13.00

Hood scoop, Shaker, Boss 302, 351                          65.00

Spoiler, rear deck, SportsRoof models only                 20.00

Steering, quick ratio(std Boss 302)                        16.00

Suspension, Competition(NA Six Cyl)                         31.00

Tachometer and Trip odometer(NA Six cyl)                   54.00

1970 Exterior Colors		    Code

Raven Black		                   	A

Dark Ivy Green Metallic			C

Yellow		                  	D

Medium Lime Metallic			G

Grabber Blue			                   I

Bright Gold Metallic			K

Wimbledon White		            	M

Pastel Blue			                    N

Medium Blue Metallic			Q

Medium Gold Metallic			S

Red			                    T

Grabber Orange		              	U

Grabber Green		               	Z

Calypso Coral		               	1

Light Ivy Yellow			          2

Silver Blue Metallic			6

1970 Interior Trim			             Code

Black vinyl			                       BA

Blue vinyl		          	         BB

Vermillion vinyl			              BE

Ginger vinyl			                        BF

Ivy vinyl			                        BG

White vinyl			                        BW

Black comfortweave vinyl		          EA

Blue comfortweave vinyl			     EB

Ivy comfortweave vinyl			     EG

White comfortweave vinyl			     EW

Black comfortweave vinyl			     TA

Blue comfortweave vinyl			     TB

Ivy comfortweave vinyl			     TG

White comfortweave vinyl			     TW

Vermillion Blazer Stripe cloth	     UE

Ginger Blazer Stripe cloth		     UF

Vermillion Blazer Stripe cloth	     CE

Ginger Blazer Strip cloth			CF

Black Houndstooth cloth & vinyl	     AA

Blue Houndstooth cloth & vinyl		AB

Vermillion Houndstooth cloth & vinyl	AE

Ginger Houndstooth cloth & vinyl		AF

Ivy Houndstooth cloth & vinyl			AG

Black Mach 1 knitted vinyl			3A

Blue Mach 1 knitted vinyl			3B

Ivy Mach 1 knitted vinyl			     3G

White Mach I knitted vinyl			3W

Vermillion Mach 1 knitted vinyl     	3E

Ginger Mach 1 knitted vinyl			3F

Convertible Top Colors

Black or White

1970 Mustang Facts

1970 Mustangs were mildly restyled. Headlight configuration reverted to single seven inch units, this time inside the grille opening. Simulated scoops took the place of the outside headlights. The rear taillight panel is flat rather than concave and the taillights are recessed.

In the interior, a new steering is used. The ignition switch is relocated on the steering column, as with all other domestic makes. The only optional interior is the Decor Group. It consists of knighted vinyl or Blazer Stripe high-back buckets, simulated wood grain appliqués on the dash, deluxe steering wheel, molded door panels with simulated wood grain appliqués, dual color-keyed racing mirrors and rocker panel and wheel lip moldings.

High back bucket seats are standard equipment on all Mustangs.

The Sport Slats and rear deck wing are optional on all Mustang SportRoofs.

The Shaker scoop was again optional on engines other than the 428. It was available with both 351s and also on the Boss 302.

The Competition Suspension was unchanged, except for the addition of a rear stabilizer bar.

The Drag Pack option, in conjunction with the optional 3.91 or 4.30 axle ratios, transformed the 428CJ into a 428SCJ, unchanged from 1969.

All 1970 Mustangs with dual exhaust systems benefited from a new exhaust system that used two mufflers mounted ahead of the rear axle, replacing the transverse muffler of previous years.

All four-speed equipped Mustangs used a Hurst shifter.

While the 390 was dropped, a new 351 joined the lineup. The 351 Cleveland, available in two-barrel and four-barrel forms(250 and 300 hp) used cylinder heads which were very similar to those used on the Boss 302. The two-barrel engines used the so-called two-barrel heads which have smaller ports and valves. The four-barrel heads have the same size valves and ports as the Boss 302 cylinder heads. The 351W 4V was dropped but Mustangs equipped with the two barrel 351 could either be a 351W or a 351C.

The Mach 1, of which 40,975 were built, was restyled, getting a revised grille that had two driving lamps. The NASCAR hood pins were replaced with twist type latches and the blacked out hood treatment of 1969 was replaced by a stripe arrangement in the middle of the hood, painted white or black. A complementary stripe was used on the rear deck lid, while the rear taillight panel got a honeycomb treatment. On the sides, aluminum rocker panel moldings with large Mach 1 lettering replaced the previous year's side tape stripes. Oval exhaust extensions replaced the quad arrangement on Mach 1s(and other Mustangs) with dual exhausts. Simulated sports wheelcovers replaced the chrome styled steel wheels, but painted styled steel wheels were a no-cost option.

According to Kevin Marti, a total of 3,959 Mustangs with the 428CJ were built; 800 of these consisted of the non-Ram-Air engine.

The Grande, of which 13,583 were built, too, was relatively unchanged. A half vinyl roof became part of the Grande package while in the interior, houndstooth cloth was used on the seats. The wire wheel covers became optional on the 1970 Grande.

The Boss 302 got a new tape stripe treatment that began on the hood (similar to the Mach 1) but then continued along the rear of the hood and down the front fenders and across the sides to the rear. Standard wheel size remained at 15x7, however a trim ring/hub cap arrangement took place of the Magnum 500s. Chrome Magnum 500 wheels, though, were optional but only on the Boss 302. The Shaker scoop was optional on the Boss 302.

Mechanically, the Boss 302 benefited from the redesigned dual exhaust system, the standard Hurst shifter, and the Competition Suspension which used a rear stabilizer bar measuring 5/8". The engine got smaller intake valves 2.19" vs. 2.23” for 1969, which resulted in slightly better throttle response. Aluminum valve covers replaced the chrome steel ones of 1969.

The 1970 Boss 429 featured a gloss black hood scoop, chrome Magnum 500 wheels that used a Boss 302 type center cap, the revised exhaust system and the Hurst shifter. Color availability was Grabber Blue, Grabber Orange, Grabber Green, Calypso Coral and Pastel Blue. Interior color selection was limited to black or white.

The 1970 Boss 429 engine was the 820-T version, however, it was fitted with a mechanical lifter camshaft, and a more efficient radiator fan. Some engines were tagged 820-A. These were 820-T engines that had some minor emission system modifications. The 3/4 inch rear stabilizer bar was replaced by the 5/8 inch unit found on other Competition Suspension equipped Mustangs.

499 1970 Boss 429s were built. KK numbers range from KK2060 to KK2558. As with 1969 Bosses, all 1970 Boss 302 Mustangs had the consecutive unit number on the engine block for additional identification. The Boss 429s had additional VIN numbers on the engine block, transmission and inner fenders.

Ford created two 1970 Boss 429 Lawmen Mustangs for tour to U.S. troops. Only one of these 1200hp survives today, and it was sold to wrestler Bill Goldberg in the 2003 Barrett-Jackson Auction.

The 1970 Grabber SportsRoof Mustang consisted of a option package that included 1969 Boss 302 side stripes (but without and Boss 302 lettering) and a trim ring/hub cap combination for the wheels. A second version used different side stripes beginning at the outside rearview mirrors and continuing to the rear. 302 or 351 lettering at the top of the stripe designated engine size.

The tilt-away steering wheel was replaced by a conventional five-position tilt steering wheel.